## Slide 1: Water Body Extraction from Remote Sensing Images USING U-NET
Study Area: Telangana

## Slide 2
Introduction
Water body extraction from satellite images is crucial for various real-world applications.
In Urban Planning, it helps manage reservoirs, lakes, and drainage systems.
In Agriculture, it supports irrigation planning and water resource monitoring.
For Disaster Management, accurate mapping of water bodies aids in flood prediction, emergency response, and environmental monitoring.

## Slide 3
Water Body Extraction Methods
Traditional Methods
  Water bodies were extracted through manual digitization or visual interpretation of satellite images.
  This process is accurate at small scales but time-consuming and not scalable for large or frequently changing regions.
Spectral-Index based Methods
  Spectral indices use reflectance properties of water in different bands.
  Popular Indices are NDWI (Normalized Difference Water Index), MNDWI (Modified NDWI),
  AWEI (Automated Water Extraction Index).
  These indices are simple to use but threshold selection is often empirical and may not generalize well.

## Slide 4
Water Body Extraction Methods
3. Machine Learning Approaches
  Classical machine learning algorithms (e.g., Random Forests, SVMs, Decision Trees) are used for water classification.
Require manual feature engineering, which may not capture complex patterns.
  Performance is sensitive to training data quality and feature selection.
4. Deep Learning Methods
  Deep neural networks learn features automatically from raw pixel data—no manual feature engineering required.
  Delivers end-to-end segmentation, outputting a pixel-wise classification map.

## Slide 5
Study Area - Telangana

## Slide 6
Data Acquisition
Satellite Source: Sentinel-2
Sentinel-2 provides multi-spectral data at varying resolutions (10m, 20m, 60m), with frequent revisit times, making it ideal for temporal and spatial monitoring.
Bands Selected: NIR and SWIR
Spatial Resolution:
  B8 (NIR) –10m
  B8A (NIR) – 20m
  B11 (SWIR) – 20m
  B12 (SWIR) – 20m
AOI: Telangana, India
These bands are selected because they support the calculation of Spectral Indices.

## Slide 7
Data Preprocessing
TIF files are present in a specific folder
(folder_id = '1vmo3Mje4Oc2klXMQHvVUx_HIIHqzSOuF')
Only the files that containing bands 8, 8A, 11, 12 are selected because of their importance in Water detection.
Then, each file is split into 512 X 512 patches using a sliding window approach which handles non-uniform image sizes by adjusting window bounds.
Patches that contain Nan value in any band of atleast one pixel are discarded.
A total of 4260 patches are generated.

## Slide 8
Data Preprocessing
For each patch, a false color composite is generated by assigning Band 8 to Red Channel, Band 11 to Green Channel and Band 12 to Blue Channel.
Normalized pixel values to the 0-255 range for saving as .png
NDWI is computed from each patch:
A combination of spectral and intensity filtering is applied:
  Identify pixels with:
    Very dark NIR reflectance (bottom 5%)
    Very dark SWIR reflectance (bottom 5%)
    High NDWI values (greater than 0.6)
  Combine with intensity thresholding (bottom 3%) for extra robustness

## Slide 9
Data Preprocessing
To clean up noisy predictions:
  Remove small objects (area < 100 pixels)
  Binary closing and opening using disk-shaped structuring elements
  Final result is a approximate clean binary water mask
Masks generated are saved as .png with 0 indicating no-water and 1 indicating water for each pixel.

## Slide 10
Some Sample Patches

## Slide 11
Some Sample Patches

## Slide 12
Some Sample Patches

## Slide 13
Some Sample Patches

## Slide 15
Model Architecture

## Slide 16
Experimental Setup
Frameworks Used
PyTorch 2.1.0.
Image and Mask Transformations
Resized the image to 512x512 pixels.
Normalized images using standard ImageNet Mean and Standard Deviation which helps in faster and more stable training.
Resized label iamge to 512x512.
Each mask pixel becomes a float value in [0, 1].

## Slide 17
Experimental Setup
Training Process
Loss Funtion: BCE (Binary Cross Entropy)
Optimizer: Adam because it is efficient and widely used in segmentation tasks.
Used a Learning rate scheduler and learning rate is changed if validation loss does not change and is used to improve the training process.
For each epoch, loss, pixel-wise accuracy, dice coefficient, IoU are calculated for both the training and validation data.

## Slide 18
Experimental Setup
Training Process
Loss Funtion: BCE (Binary Cross Entropy)
Optimizer: Adam because it is efficient and widely used in segmentation tasks.
Used a Learning rate scheduler and learning rate is changed if validation loss does not change and is used to improve the training process.
For each epoch, loss, pixel-wise accuracy, dice coefficient, IoU are calculated for both the training and validation data.

## Slide 19
Metrics Calculated for Test Data:

## Slide 20
Curves

## Slide 21
Curves

## Slide 22
Curves

## Slide 23
Curves

## Slide 24
Prediction on Test Data

## Slide 30
THANK YOU